Prop. & Trans. Delay
Hosts A→B connected by single link | if (Host→ pack at t=0) | when(t=dtrans){ endOfPack = (just leaving Host)}
$R → rate(bps) of link from A→B | if(dprop>dtrans) | when(t=dtrans){ firstBitOfPack = (in link & hasn’t reached Host(B)
$L → size of pack. Sent from A→B | if(dprop<dtrans) | when(t=dtrans){ firstBitOfPack = (just reached Host(B)
$m → meters	| if(dprop=dtrans) | $m = ($L/$R) * ($s)
$s → prop. Speed along link ($m/sec) | dtrans = L/R seconds
dprop=m/s seconds	| dend-to-end = (m/s + L/R) seconds
---------------------------------------------------------------------------------------------------------------------------------------------------
dend-to-end for packet with multiple links and switches with no queueing delays
Let di, si, Ri – length, prop speed, & transmission rate of link-i for i=1,2,…,total links | Switch delays = dproc
dproc= L/R1 + L/R2 + … + L/Rtotal-links + d1/s1 + d2/s2 + … + d(total-links)/s(total-links) + (number of switches)*(dproc)
---------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------- Queue-Delay | all packets have length L, Transmission Rate=R, x bits of the currently-being-transmitted packet have been transmitted, and n packets are already in queue
Queueing delay = (nL + (L - x))/R
---------------------------------------------------------------------------------------------------------------------------------------------------
Throughput
M = (number of client server pairs). Rs, Rc, and R are rates of the server links, client links and network link.
If all other link have abundant capacity and there is no other traffic,
Throughput = min{Rs, Rc, R/M}
If – $M Paths between the server and the client. No two paths share any link. Path k(k=1,…,M) consists of N links with transmission rates R1k, R2k,…,Rnk. (1)Server can only use one path to send data to client. (2)Server can use all M paths
(1)Max throughput = max{min{R11, R21,…,RN1},min{R12,R22,…, RN2},…,min{R1M,R2M, … , RNM}}
(2)Max throughput= summation(k=1→M) min{ R1k, R2k,…,RNk}
---------------------------------------------------------------------------------------------------------------------------------------------------
Bandwidth delay & Bit Width
Calculate bandwidth-delay product, R*dprop | R=(X)Mbps=X*(1e+6) delay = Xbits
If a file is sent continuously as one large message the maximum number of bits that will be in link=R*dprop
Bandwidth-delay product of a link is the the maximum number of bits that can be in the link.
Width of a bit(meters) in the link = length of the link/bandwidth-delay product
width of bit when (s=prop speed, R = trans. Rate) = s/R
-x=photoSize, min value of x for microwave link to be cont. Transm. ,(R=Mbps) | (R*106)(interval between photo) = X bits
----------
Packet Travel Through switches to destination
(hop occurs when a packet is passed from one network segment to the next.)	($1)Time from source to first packet = ($s = (#.#) * 10k)*/(link speed Mbps = (#.#) * 10k)= Z msec ($2)Time from source host to destination host with store-&-forward switching = (Z secs) * (X hops) = Y msec -if each pack is 10,000 bits long how long does it take to move the first packet from source host to first switch if link is 2Mbps. (1*104)/(2*106)=5msec. Second packet would be 2 * 5msec = 10msec Time for file source → destination with message sementation = ($2)+((Nth packet received)*($1)) (Pro)Message segmentation→errors aren’t tolerated→huge packet is retransmitted. (Con) Smaller packets wait in queue --------------------------------------------------------------------------------------------------------------------------------------------------
HTTP	Persistent→ forces requests and responses over one TCP connection | Non-Persistent→ sent over separate TCP connects. Date header→ object modification details. | First (X) bytes of document being returned→ chars following blank <cr><lf> Time taken for DNS look up + establish TCP connection + send&receive object → 2RTT0 + (RTT1 + RTT2 + … + RTTn)	---------------------------------------------------------------------------------------------------------------------------------------	Caching	total caching delay = Internet delay + access delay + LAN delay	access link utilization, delay with cache - (.x(percentage of requests satisfied @ orig) * (Mbps)/(Access link Mbps)
DNS	DNS name resolution: requesting host(1)→ ←(8)local DNS serv(2)→←(7)root DNS(3)→←(6)TLD DNS(4)→←(5)Authoritative DNS(dns.cs.umass.edu – gaia.cs.umass.edu)

Client Server | P2P
ui: peer I upload capacity | di: peer I download capacity | us: server upload capacity | Time to send one copy: F/us	Time to send N Copies NF/us | dmin : min client download rate | max client download time: F/dmin Time to distribute F(file size) to N clients using cli-serv approach: Dc-s>=max{NF/us,F/dmin} |	Time to distribute F(file size) to N clients using P2P approach: DP2P>=max{F/Us,F/dmin,NF/(us + summation(ui)}
--HW2
TCP handshakes, TCP closing a connection,

rdt_send()(data)→rdt send side(pack)→udt_send()→ |unreliable channel| →pac)rdt rec side→rdt_rcv()→ deliver_data()	(utilization)fraction of time sender busy sending – (L/R)/(RTT + L/R)	Cookies	Keep state at sender/receiver over multiple transactions

Chapter 3 slides
TCP close→ client.close()→FINbit=1, seq=x→ ACKbit ???
Congestion scenarios
TCP switching from slow start to CA
Cookies
Cache- at least 1 problem, how to calculate total delay (slides link 2-41)
Be very familiar with SMTP
be given wireshark info and you have to differentiate which part of the packet is tcp and which part is UDP
FSM