Test 3 Material

Transport Layer 3-105 (Important)
Why is TCP fair?
*** Be able to explain why TCP maintains fairness ***

Transport Layer 3-106
Fairness(more)
Fairness, parallel TCP connections
e.g., link of rate R with 9 existing connections:
- New app asks foor 1 TCP, gets rate R/10
- New app asks for 11 TCPs gets R/2
Transport Layer 3-107
Explicit Congestion Notification
-network-assisted congestion conrol:
- Two bits in IP header (ToS field) markd by network router to indicate congestion
- Congestion indication carried to receiving host
- receiver(seeing congestion indication in IP datagram))
- sets ECE bit on receiver-to sender ack segment to notify sender of congestion
When notified of congestion it can control speed

End of Chapter 3

Chapter 4
Overview of Network Layer
- data plane
- control plane

4-5
Two key network-layer functions
- forwarding-define
- routing -define

4-6
get 4-6 illustration
Data Plan | Control Plane

Control Planeqq
- Two control plane approaches.
1.) ?
2.) ?

5-7 Per-router control plane
illustration of forwarding table
once they have forwarding table – router will check it to see which router to forward it to
distribution algorithm – can get network info and local info only

5-8
Logically centralized control plane
(*get illustration)

Network layer: 4-9
Q: What service model for “channel” transporting datagrams from sender to receiver?

4-10
show table***

4.2 What’s inside a router

Router architecture overview 4-12
*illustration
Routing processor|routing, management control plane(software) operates in millisecond time frame
High-speed ***

Input port functions 4-13
illustration
line termination→ link layer protocol(receive)→ lookup, forwarding; queueing → | switch fabric

physical layer
data link layer
decentralized switching

decentralized switching:
-using header field values, lookup output port using forward table in input port	memory(“match plus action”)
- destination-based forwarding: forward based only on destination IP address(traditional)
- generalized forwarding

4-15
forwarding table illustration
(after table picture)
“Q. But what happens if ranges don’t divide up so nicely?”
A. More traffic(congestion) will pass through a certain interface than others. This is why we try to get things to divide evenly

4-16 IMPORTANT TO KNOW HOW TO USE PREFIX MATCHING
Longest prefix matching: when looking for forwarding table entry for given address, use longest address prefix that matches destination address.
(illustration)
 which interface?: ?
Which interface?: ?

4-17
LONGEST PREFIX MATCHING: often performed using ternary content addressable memories(TCAMs)
- content addressable: ???

4-18
Switching fabrics
crossbar type is much faster than bus and memory. If there is no cross bar???(book)
(memory, bus, and crossbar illustrations)

4-19
Switching via memory
first generation routers:
Traditional computers with switching under direct control of CPU

4-20
Switching via a bus
datagram from input port memory to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
(illustration)

4-21
Switching via interconnection network
- overcome bus bandwitdth limitations
-banyan networks, crossbar other interconnection nets intitially dveloped to connect procesors in multiprocessor
- advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric

For (4-19, 4-20, 4-21) just understand how they work

4-22
Input port queuing
fabric slower than input ports combined → queuing may occur at input queus
-queueing delay and loss due to input buffer overflow!**
- Head-of-theLine(HOL) blocking: ** queued datagram at front of queue prevents others in queue from moving forward.
(illustration)

4-23
output ports
(switch fabric illustration)
-buffering
-scheduling discipline

4-25
How much buffering?
???

4-26
Scheduling mechanisms
scheduling: choose next packet to send on link
FIFO(first in first out) scheduling: send in order of arrival to queue
- real-world example?
- discard policy:
(illustration)

4-27
Scheduling policies: priority
priority scheduling: send highest priority queued packed
- multiple classes, with different priorities
-class may depend on marking or other header info, e.g. IP source/dest, port numbers, etc
(illustration)
once it is scheduled it must finish transmission

4-28
Scheduling policies: still more
Round robin(RR) scheduling:
- multiple classes
-cyclically scan class queues, sending one complete packet from each class(if available)

4-29
Scheduling policies: still more
Wheighted Fair Queuing (WFQ):
generalized Round Robin
- each class gets weighted amount of service in each cycle
- real-world example?
(illustration)