Prop. & Trans. Delay
Hosts A→B connected by single link | if (Host→ pack at t=0) | when(t=dtrans){ endOfPack = (just leaving Host)}
$R → rate(bps) of link from A→B | if(dprop>dtrans) | when(t=dtrans){ firstBitOfPack = (in link & hasn’t reached Host(B)
$L → size of pack. Sent from A→B | if(dprop<dtrans) | when(t=dtrans){ firstBitOfPack = (just reached Host(B)
$m → meters	| if(dprop=dtrans) | $m = ($L/$R) * ($s)
$s → prop. Speed along link ($m/sec) | dtrans = L/R seconds
dprop=m/s seconds	| dend-to-end = (m/s + L/R) seconds
---------------------------------------------------------------------------------------------------------------------------------------------------
dend-to-end for packet with multiple links and switches with no queueing delays
Let di, si, Ri – length, prop speed, & transmission rate of link-i for i=1,2,…,total links | Switch delays = dproc
dproc= L/R1 + L/R2 + … + L/Rtotal-links + d1/s1 + d2/s2 + … + d(total-links)/s(total-links) + (number of switches)*(dproc)
---------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------- Queue-Delay | all packets have length L, Transmission Rate=R, x bits of the currently-being-transmitted packet have been transmitted, and n packets are already in queue
Queueing delay = (nL + (L - x))/R
---------------------------------------------------------------------------------------------------------------------------------------------------
Throughput
M = (number of client server pairs). Rs, Rc, and R are rates of the server links, client links and network link.
If all other link have abundant capacity and there is no other traffic,
Throughput = min{Rs, Rc, R/M}
If – $M Paths between the server and the client. No two paths share any link. Path k(k=1,…,M) consists of N links with transmission rates R1k, R2k,…,Rnk. (1)Server can only use one path to send data to client. (2)Server can use all M paths
(1)Max throughput = max{min{R11, R21,…,RN1},min{R12,R22,…, RN2},…,min{R1M,R2M, … , RNM}}
(2)Max throughput= summation(k=1→M) min{ R1k, R2k,…,RNk}
---------------------------------------------------------------------------------------------------------------------------------------------------
Bandwidth delay & Bit Width
Calculate bandwidth-delay product, R*dprop | R=(X)Mbps=X*(1e+6) delay = Xbits
If a file is sent continuously as one large message the maximum number of bits that will be in link=R*dprop
Bandwidth-delay product of a link is the the maximum number of bits that can be in the link.
Width of a bit(meters) in the link = length of the link/bandwidth-delay product
width of bit when (s=prop speed, R = trans. Rate) = s/R
-x=photoSize, min value of x for microwave link to be cont. Transm. ,(R=Mbps) | (R*106)(interval between photo) = X bits
----------
Packet Travel Through switches to destination
(hop occurs when a packet is passed from one network segment to the next.)	($1)Time from source to first packet = ($s = (#.#) * 10k)*/(link speed Mbps = (#.#) * 10k)= Z msec ($2)Time from source host to destination host with store-&-forward switching = (Z secs) * (X hops) = Y msec -if each pack is 10,000 bits long how long does it take to move the first packet from source host to first switch if link is 2Mbps. (1*104)/(2*106)=5msec. Second packet would be 2 * 5msec = 10msec Time for file source → destination with message sementation = ($2)+((Nth packet received)*($1)) (Pro)Message segmentation→errors aren’t tolerated→huge packet is retransmitted. (Con) Smaller packets wait in queue --------------------------------------------------------------------------------------------------------------------------------------------------
HTTP	Persistent→ forces requests and responses over one TCP connection | Non-Persistent→ sent over separate TCP connects. Date header→ object modification details. | First (X) bytes of document being returned→ chars following blank <cr><lf> Time taken for DNS look up + establish TCP connection + send&receive object → 2RTT0 + (RTT1 + RTT2 + … + RTTn)	---------------------------------------------------------------------------------------------------------------------------------------	Caching & Access link Utilization	total caching delay = Internet delay + access delay + LAN delay	access link utilization = delay with cache - (.x(percentage of requests satisfied @ orig) * (Mbps)/(Access link Mbps)
DNS	DNS name resolution: requesting host(1)→ ←(8)local DNS serv(2)→←(7)root DNS(3)→←(6)TLD DNS(4)→←(5)Authoritative DNS(dns.cs.umass.edu – gaia.cs.umass.edu)

Client Server | P2P
ui: peer I upload capacity | di: peer I download capacity | us: server upload capacity | Time to send one copy: F/us	Time to send N Copies NF/us | dmin : min client download rate | max client download time: F/dmin Time to distribute F(file size) to N clients using cli-serv approach: Dc-s>=max{NF/us,F/dmin} |	Time to distribute F(file size) to N clients using P2P approach: DP2P>=max{F/Us,F/dmin,NF/(us + summation(ui)}	c--------------------------------------------------------------------------------------------------------------------------------------------------UDP/TCP checksums | Given 3 8-bit bytes: XXXXXXXX, YYYYYYYY, ZZZZZZ	Find complement of the resultant sum – find sum of first 2 bytes, add that sum to the last byte, add carry if necessary, calculate 1’s complement of the resultant sum.	Reciever detects errors | if sum contains all 1’s then there are no errors, if sum contains at least one 0, there are errors	--------------------------------------------------------------------------------------------------------------------------------------------------Channel Utilization | CU = N * ((L/R)/((L/R)+RTT) // solve for N	if solving for window size for channel utilization to be greater than X%, plug in . X as CU in formula, solve for N (utilization)fraction of time sender busy sending – (L/R)/(RTT + L/R)
--------------------------------------------------------------------------------------------------------------------------------------------------TCP MSS trans|max value of L so TCP seq nums !exhausted. TCP seq field=4bytes| 4x8bits=32bits – 232/1024=4.19G bytes solve time L-transmit file = (232 + ((232/MSS)*(#bytes of header added to each segment)) * 8bits/((Link speed)x10Y bps) ==========================================================================================Host communcation on TCP connection |	seqence number of first segment = x, source port first segment=y, dest port =z in 2nd segment A->Bsequence number=sequence number of the $first segment + number of bytes of data in $first segment.	1st segment before 2nd : Ack#=sequence number(above formula)| 2nd segment before 1st : Ack#=x	---------------------------------------------------------------------------------------------------------------------------------------------------RTT | estimatedRTT= (1-(alpha))*EstimatedRTT+(alpha)*SampleRTT_Value | DevRTT=(1-(B)).DevRTT+B*|SampleRTT_Value-EstimatedRTT | TimeoutInterval = EstimatedRTT+4*DevRTT	----------------------------------------------------------------------------------------------------------------------------------------
Wireshark TCP Handshakes and identifying UDP parts of packet
TCP 3 way handshake(wireshark info section)	TCP 4 way handshake(wireshark info section)
57966 → 80[SYN] Seq=0 Win=65535 Len=0...	80→ 57966[FIN,ACK] seq=348 Ack=309 Win=28032
80 → 57996[SYN, ACK] Seq=0 Ack=1 Win=...	57966→80[ACK] seq=309 Ack=349 Win=131552
57996 → 80[ACK]Seq=1 Ack=1 Win=131904	57966→80[FIN,ACK] Seq=309 Ack=349 Win=131552
	80→57966[ACK] Seq=349 Ack=310 Win=28032

For sections of UDP: info will allways be something like | 51164→krb524(4444) Len = 1470 and source and destination ip addresses will be static -----------------------------------------------------------------------------------------------------------------------------------------TCP closing a connection: → = to server state; ← = to client state clientSocket.close()→FINbit=1, seq=x←ACKbit=1; ACKnum=x+1(waitForServerClose)←FINBit=1,seq=y→ACKbit=1; ACKnum=y+1 | Client state: ESTAB→FIN_WAIT_1→FIN_WAIT_2→TIMED_WAIT→CLOSED | Server state: ESTAB→CLOSE_WAIT→LAST_ACK→CLOSED --------------------------------------------------------------------------------------------------------------------------------------------------- RDT FSM (/*Illustration*/)

RDT FSM