Prop. & Trans. Delay
Hosts A→B connected by single link | if (Host→ pack at t=0) | when(t=dtrans){ endOfPack = (just leaving Host)}
$R → rate(bps) of link from A→B | if(dprop>dtrans) | when(t=dtrans){ firstBitOfPack = (in link & hasn’t reached Host(B)
$L → size of pack. Sent from A→B | if(dprop<dtrans) | when(t=dtrans){ firstBitOfPack = (just reached Host(B)
$m → meters	| if(dprop=dtrans) | $m = ($L/$R) * ($s)
$s → prop. Speed along link ($m/sec) | dtrans = L/R seconds
dprop=m/s seconds	| dend-to-end = (m/s + L/R) seconds
---------------------------------------------------------------------------------------------------------------------------------------------------
dend-to-end for packet with multiple links and switches with no queueing delays
Let di, si, Ri – length, prop speed, & transmission rate of link-i for i=1,2,…,total links | Switch delays = dproc
dproc= L/R1 + L/R2 + … + L/Rtotal-links + d1/s1 + d2/s2 + … + d(total-links)/s(total-links) + (number of switches)*(dproc)
---------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------- Queue-Delay | all packets have length L, Transmission Rate=R, x bits of the currently-being-transmitted packet have been transmitted, and n packets are already in queue
Queueing delay = (nL + (L - x))/R
---------------------------------------------------------------------------------------------------------------------------------------------------
Throughput
M = (number of client server pairs). Rs, Rc, and R are rates of the server links, client links and network link.
If all other link have abundant capacity and there is no other traffic,
Throughput = min{Rs, Rc, R/M}
If – $M Paths between the server and the client. No two paths share any link. Path k(k=1,…,M) consists of N links with transmission rates R1k, R2k,…,Rnk. (1)Server can only use one path to send data to client. (2)Server can use all M paths
(1)Max throughput = max{min{R11, R21,…,RN1},min{R12,R22,…, RN2},…,min{R1M,R2M, … , RNM}}
(2)Max throughput= summation(k=1→M) min{ R1k, R2k,…,RNk}
---------------------------------------------------------------------------------------------------------------------------------------------------
Bandwidth delay & Bit Width
Calculate bandwidth-delay product, R*dprop | R=(X)Mbps=X*(1e+6) delay = Xbits
If a file is sent continuously as one large message the maximum number of bits that will be in link=R*dprop
Bandwidth-delay product of a link is the the maximum number of bits that can be in the link.
Width of a bit(meters) in the link = length of the link/bandwidth-delay product
width of bit when (s=prop speed, R = trans. Rate) = s/R
-x=photoSize, min value of x for microwave link to be cont. Transm. ,(R=Mbps) | (R*106)(interval between photo) = X bits
----------
Packet Travel Through switches to destination
(hop occurs when a packet is passed from one network segment to the next.)	($1)Time from source to first packet = ($s = (#.#) * 10k)*/(link speed Mbps = (#.#) * 10k)= Z msec ($2)Time from source host to destination host with store-&-forward switching = (Z secs) * (X hops) = Y msec -if each pack is 10,000 bits long how long does it take to move the first packet from source host to first switch if link is 2Mbps. (1*104)/(2*106)=5msec. Second packet would be 2 * 5msec = 10msec Time for file source → destination with message sementation = ($2)+((Nth packet received)*($1)) (Pro)Message segmentation→errors aren’t tolerated→huge packet is retransmitted. (Con) Smaller packets wait in queue --------------------------------------------------------------------------------------------------------------------------------------------------
HTTP	Persistent→ forces requests and responses over one TCP connection | Non-Persistent→ sent over separate TCP connects. Date header→ object modification details. | First (X) bytes of document being returned→ chars following blank <cr><lf> Time taken for DNS look up + establish TCP connection + send&receive object → 2RTT0 + (RTT1 + RTT2 + … + RTTn) How end of a message body is marked → HTTP doesn’t mark end of body ---------------------------------------------------------------------------------------------------------------------------------------	Caching & Access link Utilization	total caching delay = Internet delay + access delay + LAN delay	access link utilization = delay with cache - (.x(percentage of requests satisfied @ orig) * (Mbps)/(Access link Mbps)
DNS Name Resolution	DNS name resolution: requesting host(1)→ ←(8)local DNS serv(2)→←(7)root DNS(3)→←(6)TLD DNS(4)→←(5)Authoritative DNS(dns.cs.umass.edu – gaia.cs.umass.edu)

Client Server | P2P
ui: peer I upload capacity | di: peer I download capacity | us: server upload capacity | Time to send one copy: F/us	Time to send N Copies NF/us | dmin : min client download rate | max client download time: F/dmin Time to distribute F(file size) to N clients using cli-serv approach: Dc-s>=max{NF/us,F/dmin} |	Time to distribute F(file size) to N clients using P2P approach: DP2P>=max{F/Us,F/dmin,NF/(us + summation(ui)}	c--------------------------------------------------------------------------------------------------------------------------------------------------UDP/TCP checksums | Given 3 8-bit bytes: XXXXXXXX, YYYYYYYY, ZZZZZZ	Find complement of the resultant sum – find sum of first 2 bytes, add that sum to the last byte, add carry if necessary, calculate 1’s complement of the resultant sum.	Reciever detects errors | if sum contains all 1’s then there are no errors, if sum contains at least one 0, there are errors	--------------------------------------------------------------------------------------------------------------------------------------------------Channel Utilization | CU = N * ((L/R)/((L/R)+RTT) // solve for N	if solving for window size for channel utilization to be greater than X%, plug in . X as CU in formula, solve for N (utilization)fraction of time sender busy sending – (L/R)/(RTT + L/R)
--------------------------------------------------------------------------------------------------------------------------------------------------TCP MSS trans|max value of L so TCP seq nums !exhausted. TCP seq field=4bytes| 4x8bits=32bits – 232/1024=4.19G bytes solve time L-transmit file = (232 + ((232/MSS)*(#bytes of header added to each segment)) * 8bits/((Link speed)x10Y bps) ==========================================================================================Host communcation on TCP connection |	seqence number of first segment = x, source port first segment=y, dest port =z in 2nd segment A->Bsequence number=sequence number of the $first segment + number of bytes of data in $first segment.	1st segment before 2nd : Ack#=sequence number(above formula)| 2nd segment before 1st : Ack#=x	---------------------------------------------------------------------------------------------------------------------------------------------------RTT | estimatedRTT= (1-(alpha))*EstimatedRTT+(alpha)*SampleRTT_Value | DevRTT=(1-(B)).DevRTT+B*|SampleRTT_Value-EstimatedRTT | TimeoutInterval = EstimatedRTT+4*DevRTT	----------------------------------------------------------------------------------------------------------------------------------------
Wireshark TCP Handshakes and identifying UDP parts of packet
TCP 3 way handshake(wireshark info section)	TCP 4 way handshake(wireshark info section)
57966 → 80[SYN] Seq=0 Win=65535 Len=0...	80→ 57966[FIN,ACK] seq=348 Ack=309 Win=28032
80 → 57996[SYN, ACK] Seq=0 Ack=1 Win=...	57966→80[ACK] seq=309 Ack=349 Win=131552
57996 → 80[ACK]Seq=1 Ack=1 Win=131904	57966→80[FIN,ACK] Seq=309 Ack=349 Win=131552
	80→57966[ACK] Seq=349 Ack=310 Win=28032

For sections of UDP: info will allways be something like | 51164→krb524(4444) Len = 1470 and source and destination ip addresses will be static -----------------------------------------------------------------------------------------------------------------------------------------TCP closing a connection: → = to server state; ← = to client state clientSocket.close()→FINbit=1, seq=x←ACKbit=1; ACKnum=x+1(waitForServerClose)←FINBit=1,seq=y→ACKbit=1; ACKnum=y+1 | Client state: ESTAB→FIN_WAIT_1→FIN_WAIT_2→TIMED_WAIT→CLOSED | Server state: ESTAB→CLOSE_WAIT→LAST_ACK→CLOSED --------------------------------------------------------------------------------------------------------------------------------------------------- RDT FSM (/*Illustration*/)

RDT FSM

HTTP Client Retrieval
HTTP client wants to retrieve document at a URL. The IP addr. Of the HTTP server is initially unknown. What transport and application-layer protocols besides HTTP are needed in this scenario?	Transport layer protocols-TCP for HTTP and UDP for DNS || Application layer protocols-DNS and HTTP	SMTP	How SMTP marks end of a message body→ (‘.’)	DNS cache calculations	If you can access the caches in local DNS servers. You can find which web servers are the most popular by using snapshots of DNS cache to count the number of requests for each web server.